## Slide 1: Fluids in Nanochannels
Suraj Singh
Guide: Prof. Rama Govindarajan (TIFRH)
3rd December, 2013

## Slide 2
According to Bernoulli's equation, Incompressible fluid will speed while converging and slow down while flowing a diverging channel.

## Slide 3
But let’s take the analogy of traffic flow. We see quite the opposite is true here. Narrower roads face a lot of traffic jams and whenever the road widens the vehicles will go at their comfortable pace and will not much affected by the other vehicles. So this effectively increases the flow velocity in diverging channels.
Well intuitively, we can see that this happens just due to increase in the inter-vehicular distance. Also our analogy to the fluid flow needs the no-slip condition at the wall boundaries to be true, which is not a constraint for the traffic.

## Slide 4: No-Slip condition
Even though this condition is widely used throughout fluid dynamics, its closest understanding we think, comes from the James Clark Maxwell’s paper of 1879.
He gives the conceptual understanding of this no slip as an outcome of constant energy loss in the molecules colliding with the walls and eventually sticking with it causing the no-slip condition.
This actually means that there is some slip but insignificant for the large scale statistics.
But if we go to molecular scales (knudsen regime) this slip becomes a significant factor.

## Slide 5: Knudsen Regime
(Regimes characterised by Knudsen numbers larger than 0.01)
Knudsen Number (kn) = l/L (l = mean free path, L = characteristic length)
Flows are characterised as:
slip flow (0.01 < kn< 0.1),
transition flow (0.1 < kn < 10) and
free-molecule flow (kn > 10).
This means that the statistical descriptions of molecular activity doesn't hold good and fluid properties such as density, viscosity, thermal conductivity, temperature, etc. cannot be expressed as continuous functions of space and time.

## Slide 6: Slip and Slip velocity

## Slide 7: What happens when we go to the molecular scales?
The question we are asking is: What happens to the flow in the nano–channels?
Beyond the Knudsen number of 0.01 the continuum description of the fluid fails to portray its behavior perfectly.
We introduce Maxwell’s slip model for incorporating the velocity slip but it works only till Kn = 0.15.
What is the way out?

## Slide 8
Problem at hand
Understanding Velocity changes and boundary slip in diverging or converging nano-channels.
This problem on continuum level was solved by Jeffery, G. B. (1915) and Hamel, G. (1916).
The solutions are more elaborately given by Rosenhead, L. (1940).
The flow is shown to exhibit from purely outward to a mixture of outwards and inwards flows depending upon angles of divergence(α) and Reynolds number(Re). Characterised by the parameter S = (α*Re)

## Slide 9: Jeffery –Hamel equations
Exact solutions have been found for this variation of Navier-Stokes equations.
Navier-Stokes in cylindrical coordinates.

## Slide 11
The molecular level picture is not understood properly as the continuum laws are valid for knudsen numbers <0.01. Whereas the flows in context have knudsen numbers far above the critical value.
Thus a molecular level approach is needed to properly model the flow. Molecular dynamics simulation seems to be the best possible way to go forward.

## Slide 12
Fluids at molecular levels can be idealized as a bunch of billiards balls trying to find their way through the geometry of the flow.

## Slide 13
Molecular Dynamics Approach
Fluid is simulated via simulating each and every molecule using Lenard-Jones potential and analysis is done.
The walls are made of closely packed molecules which are unmovable and are connected to a thermostat to keep the wall temperature constant throughout.
Fluid is also kept in isothermal condition and initially placed on a lattice with randomized velocities.
The Verlet integrator scheme is used to integrate the trajectories of each molecule and melting is done.
Velocity samples are taken once the equilibrium state is reached.

## Slide 14: Lenard Jones potential and Phase diagram

## Slide 16
Temperature is artificially controlled to be constant and kept in the fluid region of the phase space. (Koplik and Banavar).
This method has been used extensively in microfluidics and nano flows.
Video

## Slide 17
Some results show expected results
V
z

## Slide 18
Future work:
The profile will be mapped with the Jeffery-Hamel profile to fit to find the Reynold's number of the flow.
Characterizing slip near the wall boundaries for different Reynold’s numbers.
Different simulations will be run with differing parameters to observe the inverse flow near the boundaries.
Questions to be answered:
At which scale does this inversion of behavior occur? (increased velocity instead of slowing down in a diverging geometry)

## Slide 19: References
Laminar Boundary Layers – Rosenhead
Molecular dynamics of fluid flow at solid surfaces
Joel Koplik, Jayanth R. Banavar, and Jorge F. Willemsen
The relaive roles of divergence and velocity slip in the stability of plane channel flow K.C. Sahu, A. Sameen and R. Govindarajan
Jeffery, G. B. (1915), "The Two-Dimensional Steady Motion of a Viscous Fluid", Philosophical magazine, Vol. 29, pp. 455-465”.
Hamel, G. (1916), "Spiralfömrige Bewegungen zäher Flüssigheiten", Jahresbericht der Deutschen Mathematiker-Vereinigung”.
Rosenhead, L. (1940), "The Steady Two-Dimensional Radial Flow of Viscous Fluid between Two Inclined Plane Walls", Proceedings of the Royal Society of London. Series A, Mathematical and Physical Sciences.

## Slide 20
Thank you!